## Slide 1: Future mission CAMELOT for Localisation of Gamma-Ray Transients by Fleet of Cubesats
Norbert Werner, Andras Pál, Norbert Tarcai, Gábor Galgóczi, Zsolt Várhegyi, Zsolt Frei, László Kiss
Masanori Ohno, Yasushi Fukazawa, Tsunefumi Mizuno, Hiromitsu Takahashi, Koji Tanaka, Nagomi Uchida, Kento Torigoe, Kazuhiro Nakazawa, Teruaki Enoto, Hirokazu Odaka, Yuto Ichinohe
Jakub Řípa
Charles University, Astronomical Institute MTA-Eötvos Loránd University

## Slide 2: 17. 08. 2017 beginning of multi-messenger astrophysics OF GRBs
5 gravitational wave detections from BH-BH merger
EM counterpart from NS-NS merger event GW170817/GRB170817A
Large campaign of follow-up observations identified a kilonova
The gamma-ray counterpart is unusual
Regular detections/follow-up observations are needed to make progress

## Slide 3: An empty region in parameter space
Field of view (str)
Localization accuracy
4π ー
2π ー
|
No localization
|
arcmin
|
arcsec
|
degree
INTEGRAL-SPI-ACS
INTEGRAL-SPI-ACS
(w/ IPN)
CALET-CGBM
Fermi-GBM
CALET
Fermi-LAT
MAXI
Swift-BAT
Swift-XRT
No instruments with
Larger FoV (>2π str)
+
Good Loc. Acc. (arcmin)
Discovery space
AGILE
X-ray mirror, coded mask
High loc. acc., but narrow FoV
All-sky coverage
But lower loc. acc.

## Slide 4
CAMELOT: Cubesats Applied for MEasuring
and LOcalising Transients
A constellation of at least 9 satellites can provide:
all sky coverage with a large effective area
Better than 0.1 millisecond timing accuracy
~10 arcmin localisation accuracy using triangulation
Each satellite will use a standard 3U cubesat platform developed by C3S LLC for the ESA sponsored RadCube mission. The cubsesats will be equipped with a GPS receiver for precise time synchronisation and inter-satellite (Iridium NEXT) communication equipment for rapid data download

## Slide 5
Two possible detector
configurations

## Slide 6
The detector design
To maximise the effective area, the detectors based on CsI scintillators and Multi-Pixel Photon Counters (MPPC) will occupy two lateral extensions
(8.3 cm x 15 cm x 0.9 cm x 4)
The large and thin detectors with small readout area are challenging
The read out of the CsI detectors with MPPC is currently being evaluated in the lab as part of our feasibility study. The system provides a large light yield, compact readout area and relatively low operational voltage.

## Slide 7: Spectral feasibility
Preliminary!
Single channel readout
Coincidence sum
Coincidence sum (scaled)
Energy threshold of ~10 keV is achieved for both single/multi channel readout
Energy range: 10-1000 keV (TBD)
Effective area for best incident angle is estimated by the Monte-Carlo simulation, ~300 cm2 (@100 keV)
241Am
59.5 keV
Preliminary!
Torigoe+ 2018
Effective area of one satellite is comparable to two Fermi-GBM detector modules
Effective Area (cm2)
GRB incident horizontal angle (deg)
GRB incident zenith angle (deg)
Energy (keV)
100
1000
Ohno+ 2018
CsI only
CsI + Al 1mm
CsI + CFRP 2mm

## Slide 8: CAMELOT GPS time-stamping test board
Pál et al. 2018

## Slide 9: Sky visibility on 53 deg Walker Orbits
95% of the sky will be simultaneously covered by at least 5 satellites.

## Slide 10: Sky visibility on sun-synchronous polar orbits

## Slide 11: High background on polar orbits
On polar orbit, each satellite will loose ~30-40% of observing time.
On 53° inclination orbit, each satellite will loose ~20% of observing time.
Electron flux by ESA-SEE1 model at 500 km
Lomonosov / BDRG count rate in scintillator-based
GRB detector on polar orbit (~500 km).
Svertilov+ 2018

## Slide 12: What do we expect to see?
Over 300 GRBs detected per year
Many terrestrial gamma ray flashes, solar flares, soft gamma ray repeaters, X-ray binaries, etc.

## Slide 13: Timing based localisation
Hurley+13
localisation by photon arrival time
High timing synchronization by GPS + 10μ-sec absolute
timing accuracy results several arcmin localisation accuracy ?
IPN deals with:
Different clock accuracy from one
spacecraft to another
- Various time resolutions
- Uncertainty in s/c positions
for far-Earth s/c
Different energy responses of
various detectors

## Slide 14: Localisation feasibility
Time since trigger (s)
0.5
1.0
sat0
sat1
sat3
sat2
Satellite attitude, GRB position, predicted photon count/arrival time estimated using orbit and detector simulations.
GRB!
sat0 – sat1
sat0 - sat2
sat0 – sat3
10-1000 keV
Semi-major axis: 6878.14 km
Inclination: 53 deg
RAAN: 0, 120, 240
True Anomaly: 0~320
(40 deg step)
9 satellite constellation
Preliminary!
Simulated photon arrival time is estimated by the cross correlation analysis  triangulation annulus
Ohno et al. 2018

## Slide 15: Localisation algorithm
GRB position and error is estimated by simple χ2 minimization (Tanaka+ 17)
~0.1 deg1σ (~6 arcmin) accuracy is achievable for bright/high-visibility case
Best fit position
R.A. = 20.0 (+/- 0.06) deg
Dec. = 29.9 (+/-0.10) deg
Intersection of annuli
 GRB position!
How can we estimate the most probable position and error ?
*: input position
1, 2, 3 σ region
*
Preliminary!
Ohno et al. 2018

## Slide 16: Localisation accuracy
High localisation accuracy for good photon statistics (brighter/longer)
5-10 arcmin accuracy in the best case
Ten short GRBs per year localised to within 20 arcmin
Localization accuracy of our concept is examined for all short GRBs listed in Fermi 3rd GRB Catalog (Bhar+16 T90<2s: 326 events)
Ohno et al. 2018
GRB brightness (log Fluence)
GRB duration (log T90)
GRB duration (log T90)
-5
GRB brightness (log Fluence)
-5
Loc. Accur. (deg)
Loc. Accur. (deg)
NS-NS merger
GRB170817A

## Slide 17: Summary
We are proposing the CAMELOT mission, a constellation of nine 3U cubesats in three orbital planes on low Earth orbit, to provide an all-sky coverage and ~10 arcmin localisation accuracy
Each nanosatellite shall be equipped with four thin, 9 mm, and relatively large, 8.3 × 15 cm, CsI(Tl) based detectors as lateral extensions on its surface read out by MPPCs. The large thin detectors provide high sensitivity (comparable with Fermi-GBM), while leaving enough room for electronics.
Timing based localisation demands precise time synchronization between the satellites and accurate time stamping of detected photons. This will be achieved by using GPS receivers.
Rapid localisation by gamma-ray observations is critical for the study of GW sources
Rapid follow up observations at other wavelengths require the capability for fast simultaneous downlink of data for the triggered events from all satellites in the fleet. This can be achieved using satellite-to-satellite communication networks such as Iridium NEXT.
CAMELOT will also provide important secondary science, such as monitoring of outbursts of soft gamma-ray repeaters, gamma-ray flares on the Sun, terrestrial gamma-ray flashes (produced in thunderstorms), and space weather phenomena.
CAMELOT provides ample potential for international cooperation. Because the proposed fleet is scalable and extendable, we envision collaboration with future partners using different satellite designs, extending the capabilities of the constellation.
Werner et al. arXiv: 180603681
Ohno et al. arXiv: 180603686
Pal et al. arXiv: 180603685
Torigoe et al. 2018, NIMPA, in press